## Slide 1
Assignment 4 SI Engine Combustion and Causality
Arjun Darbha
Meng Tang
Venkata Vedam
Yogesh Kanabar
Zhuyong Yang

## Slide 2: Major Components of an SI Engine for Combustion and Control
Subsystem | Components | Subsystem | Components
Intake | Throttle/Intake Valve | Exhaust | Exhaust Valve
 | Temp Sensor |  | EGR Valve
 | Manifold |  | NOx Sensor
 | EGR Valve |  | O2 Sensor
 | O2 Sensor |  | camshaft
 | Air Flow Meter |  | Turbocharger
 | Turbocharger |  | Temp Sensor
 | camshaft | Combustion | Spark Plug
Injection | Fuel Flow Meter |  | Knock Sensor
 | Injector |  | Geometry
Electronics | ECU |  | 
 | Starter |  | 

## Slide 3: SI-CI subsystem comparison
Sub-Systems | Feature | SI-Engine | CI-Engine
Basic Operation | Opertaing Cycle | Otto Cycle | Diesel Cycle
 | Compression Ratio | 8-12 | 12-24
 | Operating Condition | Operates close to stoichiometric condition. | Operates majorly on the leaner side.
 | Torque Control | Air Flow is used for control | Fuel flow is used for torque control
Fuel | Fuel Property | Octane Rating-It is the Anti-Knocking capability of the fuel. A higher value is better | Cetane Rating-It is the measure of the tendency of fuel to Auto-Ignite. A higher cetane value is better
 | Fuel Delivery | Carburetor, PFI, DI | Indirect Injection, Direct Injection(DI)
 | Fuel Delivery Pressure | Up to 150 bar | Up to 2500 bar
 | AFR | 12-18 | 18-70
 | Fuel Ignition | Begins with a spark | Begins when the fuel reaches Auto-Ignition point
Intake Conditions | Air Handling | Throttled | Un-throttled except in EGR cases
 | Throttling Condition | Mostly Naturally Aspirated, sometimes Boosted | Typically Boosted
 | Air Tracking | Fuel tracks Air | Air tracks Fuel
Exhaust Manifold | Emissions | Majorly Nox, CO | Majorly Nox, PM and CO
 | After-Treatment | 3-Way catalyst | DPF,DOC,SCR,ASC
Combustion | Air Fuel Mixture Condition | Homogeneous i.e. well mixed Air and Fuel | Stratified mixing (Heterogeneous mix)
 | Combustion Control | Optimize Spark timing | Optimize Injection timing

## Slide 4: Causality diagram (Part I)
Combustion rate
Fuel consumption
CR
Atomization
AFR
Charge Energy Density
turbulence
Valve timing
Valve lift
Camshaft
Engine geometry
Injection pressure
EGR
Dilution
EGR
Load
Inlet pressure
Piston speed
Engine geometry
Mixture homogeneity
Bulk flow

## Slide 5: Causality diagram (Part II)
Knock
Stability
Mixture homogeneity
Bulk flow
Octane rating
Peak compression Pr
CR
Spark timing
EGR
EGR
Flame front
Wall temp
Mixture homogeneity