## Slide 1
Liquid Fuels
An Overview
Group 2
Graduate Student
ME-EM Department
Michigan Tech University

## Slide 2: Group Members
Last Name | First Name | Email
Darbha | Arjun | adarbha@mtu.edu
Joshi | Abhishek | aajoshi1@mtu.edu
Voshol | Brittany | bnvoshol@mtu.edu
Yang | Zhuyong | zhuyongy@mtu.edu
Desai | Chintan | cmdesai@mtu.edu

## Slide 3: Motivation
Liquid fuel – most popular source of energy – Why?
Discussion limited to liquid fuels used in automobiles
[1]
Comparison chart denoting energy densities of various energy sources
Notes: [1] - http://www.toyota.com.hk/innovation/vision/oil_alternative_fuels.aspx
Efficiency levels of E-motors are much higher than ICEs but ED values of battery are way below gasoline/diesel
ED of Li-ion is 1/50 to that of gasoline and CNG is about ¼ to that of gasoline
Hydrogen here is gaseous

## Slide 4: Goals and objectives of this discussion
We would like to analyze various fuels from different standpoints like energy density, economic viability, availability, future prospect, maintenance issues when used, safety
Our goal is to provide information on various liquid fuels and report some numbers on criteria mentioned above
Notes: Need to collect some numbers here

## Slide 5: Hydrogen
Energy density – 8.52MJ/L @ 25OC
-This value is about twice that of gasoline and diesel(43MJ/Kg)
Mass density – 0.071kg/L
Cost per liter – Ranges from $4-$12
Availability – Most abundant chemical species in the universe!
Maintenance and safety – Need a bigger tank than usual, has to be maintained at 21K, H2 is highly flammable
Future –Depends on cutting down production and maintenance costs

## Slide 6: LPG
LPG  Propane + Butane
Energy density – 26MJ/L(About 85% that of gasoline and diesel)
Cost per liter – Ranges between $2.2 - $2.7
Availability – Byproduct of petroleum refineries, lasts as long as gasoline and diesel last
Adaptability – All gasoline vehicles are adaptable to LPG(just include a toggle switch)
Safety – LPG is explosive at room temperature in the presence of an ignition source, initiates suffocation by displacing air, but…
Emissions – Significantly lower than other fossil fuels
Notes: Just mention CNG, because its transported in the form of Liquefied Natural Gas(LNG), but its not used in this form – its used as CNG

## Slide 7: Biodiesel
Energy density – 37.53 MJ/kg [?] ~11% less than petroleum diesel [A]
Gasoline Gallon Equivalent Cost – B20 was $3.82, B100 was $4.32 in Oct. 2012[B]
Availability – made from bio materials[F]
Maintenance issues – more viscous at low temperatures than petroleum diesel [A]
Safety – non-toxic, higher flash point than petroleum diesel [C]
Future – create fuel crops [A], develop process for cellulosic biomass [F]

## Slide 8: Ethanol
Energy density – 26.8 MJ/kg [E], 27-36% less energy density than gasoline[A]
Gasoline Gallon Equivalent – E85 was $4.91 in Oct. 2012 [B]
Availability – made from corn, sugar cane, potato, and similar [A]
Maintenance issues – must use converted vehicle [A]
Safety – similar to gasoline [A]
Future – Controversy over energy used to create ethanol [A][D], problems with food used for fuel [A][D]

## Slide 9: Methanol
Energy density – 19.9 MJ/kg [E]
Gasoline Gallon Equivalent – M85 Equivalent to current hydrocarbon fuels[F]
Availability – made using natural gas, coal, and biomass[F]
Maintenance issues – must use converted vehicle, more corrosive than ethanol [A]
Safety – toxicity similar to gasoline, but less likely to ignite [F]
Future – Thermo-chemical plants cost 1.8 times that of ethanol plants, no real current infrastructure[F]

## Slide 10: Bibliography
Ehsani,M., Gao,Y,., Emadi, A., Modern Electric, Hybrid Electric, and Fuel Cell Vehicles, Second Edition, CRC Press ISBN-10: 0849331544, ISBN-13: 978-0849331541 (2010).
Mi,C., Masrur, M.A., Gao, D.W., Hybrid Electric Vehicles Principles and Applications with Practical Perspectives, Wiley, (2011)
As in a report all material must have appropriate references including web content. Provide reference on slide used (e.g, Ehsani et al. 2010)