## Slide 1
Liquid Fuels
An Overview
Group 2
Graduate Student
ME-EM Department
Michigan Tech University

## Slide 2: Group Members
Last Name | First Name | Email
Darbha | Arjun | adarbha@mtu.edu
Joshi | Abhishek | aajoshi1@mtu.edu
Voshol | Brittany | bnvoshol@mtu.edu
Yang | Zhuyong | zhuyongy@mtu.edu
Desai | Chintan | cmdesai@mtu.edu

## Slide 3: Motivation
Liquid fuel – most popular source of energy – Why?
Discussion limited to liquid fuels used in automobiles
[1]
Comparison chart denoting energy densities of various energy sources
Notes: [1] - http://www.toyota.com.hk/innovation/vision/oil_alternative_fuels.aspx
Efficiency levels of E-motors are much higher than ICEs but ED values of battery are way below gasoline/diesel
ED of Li-ion is 1/50 to that of gasoline and CNG is about ¼ to that of gasoline
Hydrogen here is gaseous

## Slide 4: Goals and objectives of this discussion
We would like to analyze various fuels from different standpoints like energy density, economic viability, availability, future prospect, maintenance issues when used, safety
Our goal is to provide information on various liquid fuels and report some numbers on criteria mentioned above
Notes: Need to collect some numbers here

## Slide 5: Gasoline
Energy density – 35 MJ/L
Mass density – 0.073kg/L
Cost per gallon – around $3.30
Maintenance and safety – More volatile than diesel oil, Jet-A, or kerosene, not only because of the base constituents, but also because of additives. Volatility is often controlled by blending with butane.
In 2011, the United States consumed about 134 billion gallons of gasoline

## Slide 6: Diesel
Energy density – 34.92 MJ/L
Mass density – 0.82kg/L
Cost per gallon – around $3.50
Maintenance and safety - generally safe doesn’t burn at low temperatures. Less volatile than gasoline.
Disadvantage - In cold climates it turns into a non-flowing gel and also it’s emissions which contains harmful products.

## Slide 7
[2]

## Slide 8: Liquid Hydrogen
Energy density – 8.52MJ/L (about 25% that of gasoline)[3]
Mass density – 0.071kg/L
Cost per gallon – Ranges from $4-$12.[4]
Availability – Most abundant chemical species in the universe!
Maintenance and safety – Need a bigger tank than usual, has to be maintained at 21K, H2 is highly flammable. [5]
Future –Depends on cutting down production and maintenance costs

## Slide 9: LPG
LPG  Propane + Butane
Energy density – 24.47 MJ/L(about 70% that of gasoline)[6]
Cost per gallon – Ranges between $2.2 - $2.7 [7]
Availability – Byproduct of petroleum refineries, lasts as long as gasoline and diesel last
Adaptability – All gasoline vehicles are adaptable to LPG(just include a toggle switch) [6]
Safety – LPG is explosive at room temperature in the presence of an ignition source, initiates suffocation by displacing air[8]
Emissions – Significantly lower than other fossil fuels[8]
Notes: Just mention CNG, because its transported in the form of Liquefied Natural Gas(LNG), but its not used in this form – its used as CNG
[A]Horst Bauer, ed. (1996). Automotive Handbook (4th ed.). Stuttgart: Robert Bosch GmbH. pp. 238–
239. ISBN 0-8376-0333-1.
[B] Internet Alt Fuel Prices.com
[C] "Liquefied Petroleum Gas Specifications and Test Methods". Gas Processors Association. 2012-05-
18.

## Slide 10: Biodiesel
Energy density – 35.6 MJ/L [3] ~11% less than petroleum diesel [9]
Gasoline Gallon Equivalent Cost – B20 was $3.82, B100 was $4.32 in Oct. 2012[10]
Availability – made from bio materials such as soybeans[11]
Maintenance issues – more viscous at low temperatures than petroleum diesel [9]
Safety – non-toxic, higher flash point than petroleum diesel [3]
Future – create fuel crops [9], develop process for cellulosic biomass [11]

## Slide 11: Ethanol
Energy density – 21.17 MJ/L [12], 27-36% less energy density than gasoline[9]
Gasoline Gallon Equivalent – E85 was $4.91 in Oct. 2012 [10]
Availability – made from corn, sugar cane, potato, and similar [9]
Maintenance issues – must use converted vehicle [9]
Safety – similar to gasoline [9]
Future – Controversy over energy used to create ethanol, problems with food used for fuel [9][13]

## Slide 12: Methanol
Energy density – 15.9 MJ/L [12]
Gasoline Gallon Equivalent – M85 Equivalent to current hydrocarbon fuels[11]
Availability – made using natural gas, coal, and biomass[11]
Maintenance issues – must use converted vehicle, more corrosive than ethanol [9]
Safety – toxicity similar to gasoline, but less likely to ignite [11]
Future – Thermo-chemical plants cost 1.8 times that of ethanol plants, no real current infrastructure[11]

## Slide 13: Conclusion
Liquid fuels are currently the most dense source of energy for vehicles
Petroleum based products will eventually run out
There are several other liquid fuels besides gasoline and diesel that may help

## Slide 14: Bibliography
http://www.toyota.com.hk/innovation/vision/oil_alternative_fuels.aspx
J.D. Hughes GSR Inc, 2008
U.S. Department of Energy, Biodiesel Benefits and Considerations Internet: http://www.afdc.energy.gov/fuels/biodiesel_benefits.html, Jul. 30, 2012 [Jan. 16, 2013]
Dale R. Simbeck, Elaine Chang Hydrogen Supply: Cost Estimate for Hydrogen pathways- Scoping Analysis NREL/SR-540-32525
Andreas Zuttel Materials for Hydrogen Storage Materials Today, September 2003.

## Slide 15: Bibliography
Horst Bauer, ed. (1996). Automotive Handbook (4th ed.). Stuttgart: Robert Bosch GmbH. pp. 238–239. ISBN 0-8376-0333-1.
Internet http://Alt Fuel Prices.com
"Liquefied Petroleum Gas Specifications and Test Methods". Gas Processors Association. 2012-05-18.
Harrow, Gerry. E85 and Biodiesel Deployment National Renewable Energy Laboratory, Internet: http://www.nrel.gov/docs/fy07osti/42312.pdf, Sept. 18, 2007 [Jan. 16, 2013]
U.S. Department of Energy ,Clean Cities Alternative Fuel Price Report, Internet: http://www.afdc.energy.gov/uploads/publication/afpr_oct_12.pdf, Oct. 2012 [Jan. 16, 2013]

## Slide 16: Bibliography
Bromberg, L. and Cheng, W.K., Methanol as an alternative transportation fuel in the US: Options for sustainable and/or energy-secure transportation, US DOE, Alternative Fuels Data Center, Internet: http://www.afdc.energy.gov/pdfs/mit_methanol_white_paper.pdf, Nov. 28, 2010 [Jan. 16, 2013]
Thomas, George. Overview of Storage Development DOE Hydrogen Program US DOE, Internet: http://www1.eere.energy.gov/hydrogenandfuelcells/pdfs/storage.pdf, May 9, 2000 [Jan. 16, 2013]
Pimentel, David and Patzek, Tad W. (2005, March) Ethanol Production Using Corn, Switchgrass, and Wood; Biodiesel Production Using Soybean and Sunflower Natural Resources Research. 14(1), pp. 65-76.