## Slide 1
A PRESENTATION ON FINAL PROJECT
DEVELOPING A PHEV FROM NON-HYBRID BASELINE VEHICLE
ARJUN | VIKRANT
MS - MEEM
Michigan Tech University

## Slide 2: Group Members
Last Name | First Name | Email
Darbha | Arjun | adarbha@mtu.edu
Chiddarwar | Vikrant | vvchidda@mtu.edu

## Slide 3: Goals and objectives
Design a working hybrid model from a baseline Chevy Malibu
Objective of the project (or course) has been reduced fuel consumption (FC) without deteriorating performance
This is achieved by using enhanced technology but, most importantly, HYBRIDISATION
a
b
Notes: A - http://www.chevrolet.com/2012-malibu-mid-size-sedan/exterior-pictures.html
B - http://www.toyota.com/prius/photo-gallery.html#!photos/10/

## Slide 4: Our Car
Vehicle Type: (PHEV) |  | 
$ 26,204 |  | 
Fuel Economy |  | 
PHEV |  | 
City | 39 | (MPGe)
Highway | 29 | (MPGe)
Combined | 35 | (MPGe)
Fuel/Energy Consumption |  | 
Gasoline | 2.76 | (gal/100 miles)
Electric | 5.64 | (kW-hr/100 miles)
Blended | 2.32 | (gale/100 miles
Range |  | 
Electric/Blended (CD) | 42 | (miles)
Gasoline (CS) | 480 | (miles)
Total (CD+CS) | 522 | (miles)
CAFE Composite FE |  | 
Combined | 39 | (MGPe)
Annual Fuel Cost |  | 
Cost | 1600 | ($)

## Slide 5: Are we any good?
Chart: FE comparison
| Chevy Malibu | Our car
 | 25 | 33
Chart: Cost comparison
| Chevy Malibu | Our car
 | 22520 | 26204
Chart: 0-100 mph
| Chevy Malibu | Our car
 | 29 | 33
Chart: 60-80 mph (passing)
| Chevy Malibu | Our car
 | 6.5 | 8
Notes: Histograms/Charts comparing baseline and HEV go in here

## Slide 6: How did we get there? (Week 1)
Week 01 – (Sensitivity Analysis)
Kp and Ki in driver subsystem have been adjusted to reduce the number of errors on drive cycle. At the end of first run, Kp = 1.0 & Ki = 0.1.
But, Kp,Ki also sensitive to FC
Different sets of transmission shift logic have been tested and a new set of values determined
Transmission and performance have strong correlation. Hence, performance compliance (through PCF) and 0-100 mph were continuously monitored
Aero drag and Rolling resistance have been changed slightly to match current values on a Malibu
Alternator Gain in IC subsystem reduced by 50%

## Slide 7: Week 1 Progress
FC is sensitive to BSFC but BSFC cannot be changed unless engine technology changes
Transmission logic affects FC and also performance
Chart: % Change in FC with a 10% change in different parameters
| Kp | Ki | Cd | Rolling resistance
 | 0.023 | 0.022 | 1 | 1
Chart: Mpg comparison Week 1
| Non-optimized | Optimized | Malibu
City | 20 | 20 | 22
Highway | 27 | 29 | 30

## Slide 8: How did we get there? (Week 2)
Model has been validated against advanced technologies discussed in NAE report
CI engine has been modeled – not provided in model presented (bsfc curves and calculation details included in the report)
Impact of mass reduction, different transmission technologies, engine technologies have been tested for FC reduction and cost and values compared against NAE report values
Engine Start-Stop technology has been implemented (drive cycle and engine level) and it has been realized that it has a great potential to reduce FC in urban driving conditions
Regeneration potential has been calculated for different drive cycles

## Slide 9: Week 2 Progress
SI 2.4l I4 GDI VVT
CI 2.3l I4 TDI
UDDS
HWFET

## Slide 10: How did we get there? (Week 3)
Motor and battery critically analyzed in this week
Three different batteries provided in the model have been analyzed in terms of capacity, energy density and cost.
Battery is also tested by analyzing SOC values at the end of different drive cycles
Three different motors with different power rating have been provided. Each motor is tested in different drive cycles.
As improvement in FE is directly related to degree of hybridization, high power motor (45 kW) is deemed best suited for this purpose
Also, performance deteriorates when a low power motor is used

## Slide 11: Week 3 Progress
Chart: 0-100mph for motor TR = 0.2
| Motor-0 | Motor-1 | Motor-2
 | 43 | 38.5 | 36
Chart: Battery energy density and cost comparison
| Pb Acid | NiMH | Li-ion
Energy density | 0.20833 | 0.5 | 1
Cost | 0.33333 | 0.75 | 1
Chart: Motor comparison
| 9 KW | 30 KW | 45 KW
Torque(Scaled) | 0.048951 | 1 | 0.5
Cost(Scaled) | 0.2 | 0.66667 | 1

## Slide 12: How did we get there? Week 4
Implementation of hybridization has been performed so that maximum FE can be achieved
Broadly, two different approaches have been used synergistically to achieve maximum efficiency
Torque Blend Approach: The motor provides maximum torque at low rpms. This can be used for our benefit
IC Engine speed optimization: Once torque blend is employed, engine is made to operate at the most efficient point
SOC controller: A control strategy is employed to control battery SOC so that it never falls beneath 0.3 (minimum battery SOC)
Regeneration: Limit has been set on regen, no regen below 5 mph and no regen beyond SOC = 1 (overcharging!)

## Slide 13: Torque Blend approach
Blend Starts
Blend Stops
Engine starts
As the engine is not efficient in processing torque request(TR) at low RPM, Motor processes torque request in this region

## Slide 14: IC Engine Speed Optimization
Vehicle speed is scattered on the
efficiency contour
Engine speed is not controlled in
this case
Engine speed is controlled.
When engine speed is between
0 & 2500rpm with positive TR,
TR is processed at 1200 rpm

## Slide 15: Need for IC optimization
Most engine speeds in UDDS
are in 1000-1500 rpm range
Hence running at an optimal
1200 rpm
Most of the engine TR is
quite low and engine
Inefficient, hence hybridization helps

## Slide 16: Thanks for Listening